UTTAR PRADESH COOPERATIVE SUGAR FACTORIES FEDERATION LTD

9-A, RANA PRATAP MARG LUCKNOW

Ref no. P-   1585  /UPF(CP)/2012-13                             Dated: 16.8.12

M/s …………………………….                                   Tender fee : Rs 500/-

………………………………….                                   (Non refundable)

………………………………….

SUB: TENDER DOCUMENTS FOR SUPPLY OF SUGAR BAG STACKER

The technical bid, Commercial bid and EMD should be kept in a separate sealed envelope mentioning the name of item i.e. Tender for supply of SUGAR BAG STACKER on each envelope so as to reach the under signed positively up to 12.00 Noon. The schedule for Technical bid opening, commercial bid opening, Negotiation etc is given as under:-

------------------------------------------------------------------------------------------------------------

Date			Time

------------------------------------------------------------------------------------------------------------

Tender Receiving				       28.8.2012			12.00 Noon

Technical bid opening & discussion		       28.8.2012			12.15 P.M

Commercial bid opening		                   28.8.2012			3.00 P.M

------------------------------------------------------------------------------------------------------------

1-	Tender has to be submitted as per specification, terms and conditions given in

enclosed documents.

2-	Draft for EMD of  R s 25,000/- drawn on any Nationalised Bank in favour of U.P.

Cooperative Sugar Factories Federation Ltd, Lucknow must be enclosed with the

tender, without which tender will not be considered.

3-	We are enclosing herewith checklist and the tenderers are requested to furnish

complete information as per checklist along with supporting documents without

which the tender may be liable to be rejected.

4-	Tenderers are required to sign on each photocopy document attached with the tender.

( K. K . SRIVASTAVA )

GENERAL MANAGER(P)

U.P.COOPERATIVE SUGAR FACTORIES FEDERATION LIMITED

9-A, RANA PRATAP MARG, LUCKNOW

TECHNICAL BID

Name of the party……………………………………………………………………..

With  address     ……………………  … ………………………………………

SUB:- TENDER FOR SUPPLY OF  SUGAR BAG STACKER

SPECIFICATIONS:

The detailed specifications are attached herewith as on Annexure  "A".

TERMS AND CONDITIONS:

1- The tenderer should be manufacturer of above sugar machinery items for which a proof of manufacturing certificate from SSI/NSI/DI should be enclosed with the tender without which no tender shall be considered.

2- The tenderer should have an adequate experience of at least three years for supply & installation of such items to sugar factories or complete plant suppliers for which past order copies along with their performance certificates to be enclosed with the tender, the tender without past experience may not be considered for sugar machinery item

3- The party approved by M/s National Federation of Cooperative Sugar Factories Federation  New Delhi shall be preferred for consideration.

4- The tender should have the same specifications and scope of supply as given in our tender form. The tender having different specifications shall be liable to be rejected.

5- The drawing of equipment( if applicable) shall have to be submitted for approval to be concerned  factory prior to start of fabrication work.

6- The Inspection prior to dispatch the equipment shall be done by respective mill society/ Sugar Federation  for which at least 15 days clear notice to be given to the concerned unit.

7- The Federation reserves all rights to accept or reject any tender without assigning any reason thereof in the interest of mill society/Federation.

N.B:- The tender without above details and supporting documents to the satisfaction of Federation shall not be entertained for consideration in commercial bid.

All above terms & conditions are acceptable to us.

………

Date:					      Signature of the Representative

with seal

SPECIFICATION OF SUGAR BAG STACKER(DOUBLE TYPE)

( TRUCKLOADER &  CUM STACKER)

For Sampurnagar Sugar mill

1.	Frame					Heavy Duty

2.	Capacity				600-700 bags/hr

3. 	Length of stacker			15.00 mtr.

4.	Length of truckloader boom		5.00 mtr

5.	Type					Slate( one M.S & one wooden)

6.	Speed					20-30 m per minute

7.	Width of stacker			700 mm

8.	Minimum height of feed point	750 mm

- Minimum height of discharge point   2.4 m of loader & 3.5 m of stacker

- Maximum height of discharge point

a) Total stacker				10 m

b) Truck loader				3.5 m

11.	Size of sprockets			M.S 400 mm dia/15 teeth

12.	Size of M.S slates			660x50x25x2.5mm thick

13.	Size wooden slate(Bakli wood)          660 x50 x30 mm

14.	Chain material				750 mm pitch C-30,Pin EN-9,14.5 mm

dia having 38.00 mm width & 6 mm thick

chain slate. The chain will be having pin/

bush rollers.

15.	Frame					M.S.Fabricated 40x40x4 mm angle,

30x6 mm flate of runner,100x50 mm,

75x40mm & 150x75 mm chanels. The

frame of stackers part is mounted on two

sets of rubber tyre wheels having 8.00-19.00

& 7.00-19.00 tyres.Where as the truckloader

part is mounted on one set rubbe tyre wheels

& one set fabricated wheels 7.00 19.00 tyres

16.	Drive motor(Stacker part)		5.00 H.P,1440 RPM

(Kirloskar/Crompton)

Truckloader part			3 HP,1440 RPM Kirloskar/Crompton

17-	Gear box( stacker parts)		U-400 Redicon/Elecon

Truckloader part			U-300 Redicon/Elecon

For Ramala sugar mill

1-         Type					Twin  Conveyor belt type

2-	Width					600 mm

3-	Length of stacker			36 feet

4-	Capacity				600 Bag per hour

5-	Type of Bag				Jute of 100/ 50 Kg.Bag

6-	Conveyor belt heavy duty		6 ply end less 650 mm width

Dunlop/Hindustan

7-	Minimum Height			1.5 Mt.

8-	Maximum Angle			40 Degree

9-	Reduction gear box & motor size       U-600,7.5 H.P 1440 V.P.

Squirrel cage motor.

## SPECIFICATION OF TWIN BOOM STACKER FOR BAGPAT UNIT

1-	Capacity				600 Bags/Hr.

2-	Length					14.50 Mtr.

3-	Type					Slate( one M.S x one wooden)

4-	Width of Stacker			700 mm

5-	Speed					20-25 Mtr/Min.

6-	Height of Feed point			0.750 Mtr.

- Minimum Height of Discharge Point 3 Mtr.

- Max Height of Discharge Point	10 Mtr.

- Dia of Sprocket			400 mm /15 teeth.

- Size of M.S.Slate			660x50x25x2.5mm thickness

- Size of Wooden Slate			660x50x30 mm

- Heavy duty chain material		75mm pitch,C-30,Pin EN-8x14.5mm

Chain slate 6mm thickness, the chain

will be pin,bush & roller

13-	Frame					M.S. Fabricated of 40x40x4 mm thickness

boom angle,30x6 flat runner,ISMC 75,100

150 channel used mounted one set of M.S

wheel front,back side of rubber type wheel

size 700-50-16

14-	Drive motor				7.5 H.P x 1440 RPM, Kirloskar/Crompton make

15-	Gear Box				U-500,40:1(Premium Transmission make)

16-	Starter(D.O.L)				Main switch with overhead relay siemens/

L& T make.

17-	Cable					20 Meter length of 3 x 10 mm2

Stacker should be easily transportable from one Godown to an another godown by tyre wheel

U.P.COOPERATIVE SUGAR FACTORIES FEDERATION LIMITED

9-A, RANA PRATAP MARG, LUCKNOW

COMMERCIAL BID

- Name of the Party …………………………………………………………………….

- With address        ………………………………………………………………………

PARTICULARS							RATES

Sugar bag stacker	(Sampurnagar)			Rs……………………….

(Ramala)                                 Rs……………………….

(Bagpat)                                  Rs……………………….

TERMS AND CONDITIONS:

1. 	Price					F.O.R.Destination

2. 	Packing & forwarding			Inclusive

3.	Insurance Charges			Inclusive

4.	Sales Tax				Inclusive

5.	Excise Duty				Inclusive against modvat benefit.

6.	Transportation Charges		            Inclusive

7.	Terms of Payment			10% advance against Bank guarantee, balance

against delivery.

8.	Delivery Period				………………………..

( including erection & commissioning)

9.	Bank Guarantee			a- 5% for timely delivery.

b- 5% for satisfactory performance.

10.	Erection & commissioning Charges	…………………………….

11.	Total prices( including all above		…………………………….

above charges.

12.	Warranty period			Two years

13.	Validity of offer			90 days

OTHER TERMS AND CONDITIONS:

1. The price quoted should be F.O.R.Destination basis including packing & forwarding, Insurance ,Sales tax, Excise Duty & Freight charges.

2. The supplier shall have to submit 5% for delivery guarantee and 5% for satisfactory performance as our standard proforma's attached herewith.

3. The advance ( i.e 10% only) shall be released by the concerned units only after receipt of bank guarantee of equal amount. In no case more advance shall be given.

4. The rates should be given as per our terms mentioned above. The conditional offer shall be accepted.

All above terms & conditions are acceptable to us.

Dated:								Signature of the Representative

with seal.

# ANNEXURE “B”

GENERAL TERMS AND CONDITIONS FOR CAPITAL ITEMS

- Only the manufacturer which are fulfilling the required conditions of tender document are eligible to participate in the tender.

- The offer should be supported by adequate past experience of the items for which the past order copies & their performance certificate should be attached with the tender, without which the tender may be liable to be rejected.

- The terms & conditions of tender document should be duly stamped & signed .

- The tenderer should submit the tender only in prescribed original tender form issued by the U.P.Cooperative Sugar Factories Federation Lucknow. The tender document are not transferable.

- i) PRICE : The rate mentioned in the tender shall remain firm, no escalation shall be given.

ii) TAXES & DUTIES: The present rate of excise duty, taxes etc. should be clearly mentioned, however, the change in the taxes & duties may be accepted provided documentary proof for the same is submitted for approval.

- TERMS OF PAYMENTS : Terms of payment should be followed as per our tender or mutually agreed at the time of negotiation.

- NEGOTIATION OF DOCUMENTS: The following documents should be forwarded through respective banker of the factories

- Original Invoice ( two copies)

- Railway Transport Receipt.

- Packing list in duplicate.

- DELIVERY PERIOD: Delivery period shall start from the date of receipt of technically and commercially completed and confirmed order by the suppliers from the concerned factory, along with advance if necessary.

Delivery period should be adhered to strictly by the supplier as per order

of the factory copy of the delivery challan must be attached with bills.

The goods must be delivered within stipulated period mentioned in our order failing which the buyers reserve the right to return the goods at the cost and expenses of the supplier and recover all losses from the suppliers in arranging ,supply from other source without any prior notice to the supplier. The loss may be calculated by the factory based on utility of items coupled with the effect on crushing and reproduction.

The buyer also reserves the right of cancelling the order if goods are not supplied within the stipulated delivery period and would be entitled to get refund of the amount paid against the order along with all expenses incurred by the buyer in addition to loss mentioned above. The buyer shall also be entitle charge interest at bank rate on the amount of advances already paid after the expiry of the due date of delivery.

In case of late delivery and if the factory accepts the material due to any unavoidable circumstances the liquidated damages for delayed delivery at the rate of 0.5% per week for un supplied part subject to maximum of 5% will be charged by the concerned factory.

- PACKING & FORWARDING: The supplier should ensure dispatch of material ( as

per direction of mills) in secured and sound packing conditions to avoid any damage

during transit. The packing list will be kept inside each packet to factories for easy

checking of material at the time of opening at factory stores.

- INSURANCE:  The supplier will insure the material to avoid any loss or damage during transit. The charges will be paid by supplier/ factory as the case may be on presentation of necessary certificate of document stipulated in the tender form.

- DESPATCH OF MATERIAL:  The material should be despatched as per instruction given by the factory concerned. However any material sent by road transport should be sent through reputed transport company. Copy of the invoice should also be sent to this office accordingly.

- QUALITY OF MATERIAL: The material should strictly conform to the specification given in the tender. The authorised representative of mill society/ National Federation may inspect the material as per tenders before taking delivery of the same. The supplier has to provide all necessary facilities in the process of inspection. The sub-standard material and material not confirming to the specifications will be rejected by the mill society. The supplier will arrange  the transport of rejected material at their own cost and risk within 15 days from the factory premises and suitable penalty shall also be imposed on supplier due to the losses occured for want of material in the factory. Further the case shall be referred to sugar Federation Lucknow for Black list/ debarring the supplier for future dealing. For checking of the geniuness of the supplier material, the sample may be taken and sent to the concerned principal manufacturer. In case the supplied material is found spurious, the same shall be returned by the factory. The losses on account of cost of material along with interest 18% shall be recovered from the party.

- QUANTITY:  The supply of material shall be made as per quantative requirement given in order. The excess quantity of supply without consent of the  factory will not be accepted and will have to be taken back by supplier at their own cost and risk.

- SANCITY: The purchase order is final agreement between supplier & the mill society. Any terms & conditions of enquiry/ letter, Tender /Quotation or any other documents inconsistent with the terms of purchase order will have no effect and will be null and void.

- EARNEST MONEY: The tenders without requisite amount of earnest money shall not be accepted for consideration. However Government Agencies are exempted from this conditions. The earnest money of successful tenderer shall automatically be converted into security deposit will be refunded to them without interest only after satisfactory performance. If tenderer /Seller is found defaulter in supplying material as per terms of order, their earnest money (Converted into security deposit) shall be forfeited. The earnest money will be refunded without interest to the tenderers in whose favour award of order is not decided.

- The supplier shall provide all necessary documents such as excise gate pass etc to our units (Purchaser) for enabling them to obtain MODVAT facility from the excise department wherever applicable. The supplier should also mention subheading chapter of excise so that our factories may claim MODVAT facility on the material purchase.

- If required the parties may be called for further negotiation ( i.e. technical as well commercial discussion) for which right is completely reserved with the committee and which will depend  upon rates past experience and reputation of the party, otherwise the decision may be taken on tender basis.

- If you offer lower rates to any other department, the same will be given to us also. In case you do not give us the same, your order shall be cancelled with immediate effect & your tender may also be not considered to future.

- The supplier has to certify  that they had not supplied/would not supply the material, for which order has been issued from Federation at any less rate than contracted with Federation to any other Govt. or other Pvt. Parties during the validity period of order. In case of price, differential price of the manufacturer is not allowed & in case the same is delegated in the market, the EMD of the party shall be forfeited , besides debarring the party from further commercial dealings with Federation.

- JURISDICTION: The M.D U.P.Cooperative Sugar Factories Federation will be the sole arbitrator to resolve all disputes arising out of the agreement and the decision taken by the arbitrator shall be the final & acceptable to both the parties ( i.e seller and purchaser).

21.Normally negotiation of rates shall not be done ,if required, negotiation of rates can be done only with L-1 party.

GENERAL MANAGER(P)

All above terms & conditions are acceptable to us

SIGNATURE OF REPRESENTATIVE

WITH SEAL OF THE FIRM

ANNEXURE 'D'

DETAILS OF DOCUMENTS TO BE SUBMITTED ALONGWITH TENDER

1. E.M.D : D.D No & date

Bankers Name.

2.  UPST/CST Number( attached photocopy).

3.  Income Tax Clearance Certificate

4.  Turn Over to the firm

2008-09

2009-10

2010-11

5.  Past three years order copies along with performance.

6. Past three years order copies with performance certificate supplied to Cooperative/Corporations sugar mill.

7.  Authority of the firm/company authorizing tenderer to submit tender and for  negotiations.

8.  Manufacturers authorization in favour of the firm for dealship  stockist if applicable.

9  Details of works and office with name of person address, telephone no. etc email and website      address.

10. Status of the company along with names of Directors/Partners/Proprietor along with documents.

11. Copy of certificate obtained from National/International (ISO) if any.

12. Last Audited balance sheet of the manufacturer and Authorised dealer.

13.  Excise Registration certificate.

…………